## Slide 1: Protocol Stack Architecture
P
L2CAP
PHY
P
P
P
...
LL
HCI
SM
GATT
GAP
APP
ATT
Host
Controller
Apps
Notes: Provides the capability of updating code in deployed devices without the cost of physical access
Two different methods
  Over-the-air BootLoader (OBL)
    Image is downloaded and overwrites the run-code image
    Maximum image size is slightly less than half of the available flash
  Boot Image Manager (BIM)
    Provides the flexibility of having two valid images, each capable of running on reset
      Either image can execute an OAD on the other
      Possible use cases
        Dual stack (proprietary & BLE)
        Dual image with selection made at boot-time (ex. heart-rate sensor & glucose sensor)
    By restricting one of the images to a small, resident “OAD-only image,” the application image can be much larger than half of the available flash

## Slide 2: TI Bluetooth low energy Hardware
SPP
Attribute Profile
Classic
蓝牙 BR/EDR
RFCOM
L2CAP
Link Manager
BR/EDR PHY
SPP
RFCOM
Attribute Protocol
Bluetooth Smart Ready
蓝牙4.0双模
L2CAP
Link Manager
BR/EDR + LE PHY
Link Layer
LE PHY
Link Layer
L2CAP
Attribute Profile
Attribute Protocol
Bluetooth Smart
BLE单模
Notes: The ”single device solution” solution would be to use our flash based System-On-Chip as it’s true intent, put the complete solution in it. It will have the stack and application running on it.
The ”Dual Device solution” is a way for you to let the application run on another device, for example, if you would want to add bluetooth low energy functionality to an already existing design. Using a network processor configuration allows an external application and profiles to communicate by means of vendor-specific HCI commands using a hardware or UART interface, or using a virtual UART interface over USB. In these cases, the application can be developed externally while still running the Bluetooth low energy stack on the CC2540 or 41. This is the solution used with our CC2540 USB Dongle in the CC2540DK-MINI kit as we will see in a moment.

## Slide 3: Physical Layer (PHY)
RF Specifications
  Operates in 2.4 GHz ISM band
  GFSK modulation
  40 channels with 2 MHz spacing
    3 fixed advertisting channels for broadcasting, which avoid 802.11 interferance
    37 adaptively frequency hopped dynamic data channels
Physical layer can be combined with standard Bluetooth RF in a dual-mode device
2 MHz spacing allows for better adjacent channel rejection
11
6
1
P
L2CAP
PHY
P
P
P
...
LL
HCI
SM
GATT
GAP
APP
ATT
Notes: Provides the capability of updating code in deployed devices without the cost of physical access
Two different methods
  Over-the-air BootLoader (OBL)
    Image is downloaded and overwrites the run-code image
    Maximum image size is slightly less than half of the available flash
  Boot Image Manager (BIM)
    Provides the flexibility of having two valid images, each capable of running on reset
      Either image can execute an OAD on the other
      Possible use cases
        Dual stack (proprietary & BLE)
        Dual image with selection made at boot-time (ex. heart-rate sensor & glucose sensor)
    By restricting one of the images to a small, resident “OAD-only image,” the application image can be much larger than half of the available flash

## Slide 4: TI Bluetooth low energy Hardware
Preamble
1
Access Address
PDU
4
2-257
3
CRC
byte
LSB
MSB
Notes: The ”single device solution” solution would be to use our flash based System-On-Chip as it’s true intent, put the complete solution in it. It will have the stack and application running on it.
The ”Dual Device solution” is a way for you to let the application run on another device, for example, if you would want to add bluetooth low energy functionality to an already existing design. Using a network processor configuration allows an external application and profiles to communicate by means of vendor-specific HCI commands using a hardware or UART interface, or using a virtual UART interface over USB. In these cases, the application can be developed externally while still running the Bluetooth low energy stack on the CC2540 or 41. This is the solution used with our CC2540 USB Dongle in the CC2540DK-MINI kit as we will see in a moment.

## Slide 5: TI Bluetooth low energy Hardware
PDU Type
RFU
reserved for future use
TxAdd
RxAdd
bits
LSB
MSB
Length
RFU
4
2
1
1
6
2
Preamble
1
Access Address
Header
4
0-255
3
CRC
byte
LSB
MSB
Payload
2
Notes: The ”single device solution” solution would be to use our flash based System-On-Chip as it’s true intent, put the complete solution in it. It will have the stack and application running on it.
The ”Dual Device solution” is a way for you to let the application run on another device, for example, if you would want to add bluetooth low energy functionality to an already existing design. Using a network processor configuration allows an external application and profiles to communicate by means of vendor-specific HCI commands using a hardware or UART interface, or using a virtual UART interface over USB. In these cases, the application can be developed externally while still running the Bluetooth low energy stack on the CC2540 or 41. This is the solution used with our CC2540 USB Dongle in the CC2540DK-MINI kit as we will see in a moment.

## Slide 6: TI Bluetooth low energy Hardware
LLID
ENSN
SN
MD
bits
LSB
MSB
RFU
Length
2
1
1
1
3
8
Preamble
1
Access Address
Header
4
0-251
3
CRC
byte
LSB
MSB
Payload
2
MIC
4
Notes: The ”single device solution” solution would be to use our flash based System-On-Chip as it’s true intent, put the complete solution in it. It will have the stack and application running on it.
The ”Dual Device solution” is a way for you to let the application run on another device, for example, if you would want to add bluetooth low energy functionality to an already existing design. Using a network processor configuration allows an external application and profiles to communicate by means of vendor-specific HCI commands using a hardware or UART interface, or using a virtual UART interface over USB. In these cases, the application can be developed externally while still running the Bluetooth low energy stack on the CC2540 or 41. This is the solution used with our CC2540 USB Dongle in the CC2540DK-MINI kit as we will see in a moment.

## Slide 7: TI Bluetooth low energy Hardware
Primary
Battery
Service
8
Access Address
Header
32
8
8
reference
bits
LSB
Secondary
Temperature
Service
Primary
Temperature
Service
Notes: The ”single device solution” solution would be to use our flash based System-On-Chip as it’s true intent, put the complete solution in it. It will have the stack and application running on it.
The ”Dual Device solution” is a way for you to let the application run on another device, for example, if you would want to add bluetooth low energy functionality to an already existing design. Using a network processor configuration allows an external application and profiles to communicate by means of vendor-specific HCI commands using a hardware or UART interface, or using a virtual UART interface over USB. In these cases, the application can be developed externally while still running the Bluetooth low energy stack on the CC2540 or 41. This is the solution used with our CC2540 USB Dongle in the CC2540DK-MINI kit as we will see in a moment.

## Slide 8
Standby
Standby
Advertising
Scanning
Standby
Initiating
Connection
Connection

## Slide 9: BLE Link Layer: State Flow Chart
TI Information – Selective Disclosure

## Slide 10: BLE Link Layer: Advertisement Intervals
TI Information – Selective Disclosure
During one “advertising event”, an advertisement packet is transmitted on each of the three advertising channels (37, 38, and 39)
The advertising device has an “advertising interval”, which can be any amount of time between 20ms and 10.24s
The Link Layer generates a pseudo-random amount of time between 0ms and 10ms (“advertising delay”) during each advertising event. This delay is added to the advertising interval before the next advertising event, in order to prevent “beating” from multiple devices

## Slide 11: BLE Link Layer: States Flow Chart
TI Information – Selective Disclosure

## Slide 12: BLE Link Layer: Scanning
Passive Scanning
  Scanner listens on advertising channels for advertising packets
  When an advertisement packet is received, it passes the information up to the host
Active Scanning
  Scanner listens on advertising channels for advertising packets
  When an advertisement packet is received, it responds with a “scan request” packet
  Advertiser then responds back with a “scan response” packet (this packet can contain additional data from advertiser)
TI Information – Selective Disclosure

## Slide 13: BLE Link Layer: States Flow Chart
TI Information – Selective Disclosure

## Slide 14: Link Layer (LL) – Connection Events
All communications between two connected devices occur in
Connection Events
  Occur even when one (or both) sides have no data to send
  Occur periodically
Connection interval
Connection Events
time
Current draw
[mA]
Notes: All communications between two connected devices occur in “connection events”. These connection events occur periodically, with a connection interval parameter specifying the period
Each event occurs on one of the 37 data channel and the Master always communicates first and then the slave. They can continue to communicate back and forth as much as they want during one connection event. The limitation is in the radio buffer.
Connection events occur even when one (or both) sides have no data to send. This ensures that the link is still valid and if a certain number of user defined connection events occur with no acknowledgment, the connection will be considered lost by both devices.
The illustration shown is based on a real measurment of the current draw. As you can see, the device spends a lot of time in sleep which is typically around 1uA. This is the main reason why Bluetooth low energy really is low power. In the zoomed in part you can also see the power profile when slave device wakes up, does some processing, goes into RX then TX and then goes back into sleep after some post processing.

## Slide 15: Link Layer (LL) – Initiator
Connection Parameters
  Channel Map: Which data channels are used during the connection
  Hop Increment: Random value (5-16) for channel selection algorithm
  Connection Interval: Multiple of 1.25ms in range of 7.5ms and 4.0s
  Supervision Timeout: Multiple of 10ms in the range of 100ms and 32.0s
    SupervisionTimeout > (1 + SlaveLatency) * (2* ConnInterval)
  Slave Latency: Any value between 0 and 499.
SlaveLatency < ((SupervisionTimeout / ConnInterval) – 1)
PHY
Link Layer
HCI

## Slide 16: BLE Link Layer: Slave Latency
16
M
S
M
S
M
S
No slave latency – slave responds with empty packets every connation interval.
M
S
Slave latency on. Slave can skip n connection events. Only wake up if slave has data to send.
Event
Data to
Send
Event
Data to
Send
M
S
M
S
M
M
M
S
M
Slave Latency = OFF
Slave Latency = ON
TI Information – Selective Disclosure
Notes: 16

## Slide 17: BLE Link Layer: Connection Update Request
The master device can send a connection update request to the slave at any time to change any of the connection parameters (interval, slave latency, supervision timeout) at any time
At the link layer, connection parameter updates are always initiated by the master, but a higher layer protocol (L2CAP) allows a slave to request the master to send a connection update
The ability to change parameters in the middle of a connection allows for dynamically adjustmenting the power / latency / throughput tradeoffs as required by the application
TI Information – Selective Disclosure

## Slide 18: BLE Link Layer: Connection Termination
A connection can be voluntarily terminated by either the master or the slave for any reason
  One side initiates termination, and the other side must respond accordingly before both devices exit the connected state
Connection can also be terminated as a result of a supervision timeout
  The supervision timeout parameter specifies the maximum amount of time that either the master or slave can go before receiving a link-layer packet
  Supervision timeout value must be greater than the effective connection interval and less than 32.0 seconds
  Both slave and master device maintain their own “Supervision timer”, which resets to zero every time a packet is received
  If supervision timer ever reaches the supervision timeout, the device considers the connection lost, and exits the connection state (returning to the advertising, scanning, or standby state)
TI Information – Selective Disclosure

## Slide 19: Host Controller Interface (HCI)
Reused from standard Bluetooth specification,
  additional commands for LE-specific functions
Thin layer; doesn’t perform any processing
In a dual-chip solution (with separate host and controller) allows for host to communicate with controller over a standard interface (UART, USB, SDIO, etc.)
Used internally by the TI BLE protocol stack
  communication between higher and lower layers
  custom “vendor-specific commands” which can be used by an external source to directly interface with the entire stack or application. (Network Processor)
P
L2CAP
PHY
P
P
P
...
LL
HCI
SM
GATT
GAP
APP
ATT

## Slide 20: Host
The host uses the HCI API to communicate with the lower layers
The different layers of the host stack manage control messages, event messages, and transmission of data
P
L2CAP
PHY
P
P
P
...
LL
HCI
SM
GATT
GAP
APP
ATT

## Slide 21: Security Manager (SM)
Performs authentication and key management
Uses AES-128 as the encryption algorithm for security procedures
Defines protocol to setup secure link
Enabled relationships between devices:
  Pairing: encryption between two devices once a connection has been established between them
  Authentication: verifying that a peer device can be trusted. Provides protection against “Man-in-the-Middle” attacks
  Bonding: long-term relationship between devices; security and identity information is saved for re-use next time the devices are connected
P
L2CAP
PHY
P
P
P
...
LL
HCI
SM
GATT
GAP
APP
ATT

## Slide 22: BLE Security Manager Protocol (SMP): Pairing
Pairing can be initiated by either the central or peripheral device
During pairing, the two devices generate and exchange short-term keys (STK) which can be used to decrypt data packets
In addition, either device can request to enable “bonding” to create a long-term relationship between the two devices
  A long-term key (LTK) is generated, exchanged, and stored allowing device to re-encrypt the link quickly upon re-connection, without going through the complete pairing process once again
  Profile / Service configuration data is remembered, so that the user does not need to re-configure the device every time they re-connect
TI Information – Selective Disclosure

## Slide 23: BLE Security Manager Protocol (SMP) : Authentication
During the pairing process, each device states whether it wants authentication to the other device
Each device also states it’s input/output capabilities from among these options:
  DisplayOnly – no way user can input anything into device, but it can output data
  DisplayYesNo – user can input “yes” or “no” but nothing else; can also display data
  KeyboardOnly – user can input a password or PIN, but no display
  NoInputNoOutput – device has no means for user input, and has no display
  KeyboardDisplay – device has a means for display as well as for input
Based on the combination of the capabilities of the two devices, one of two methods of pairing will be used:
  Passkey entry – one device will display a randomly generator passkey, while the other will require the user to input the passkey. This allows for an authenticated link (MITM protection)
  “Just Works” – the pairing process completes without requiring a passkey to be entered. The link will not be authenticated, but is encrypted
If either one of the two devices does not require authentication, then Just Works will be used by default, allowing the user to skip passkey entry
TI Information – Selective Disclosure

## Slide 24: Attribute Protocol (ATT)
An attribute is a discrete value (Data) that has the following three properties associated with it:
  A handle (address)
  A type (UUID)
  A set of permissions
ATT defines the over-the-air protocol for
  Reading
  Writing
  Discovering attributes
Allows for different permissions to be assigned to attributes
  Readable
  Writeable
  Protected (Additional security is required for access)
P
L2CAP
PHY
P
P
P
...
LL
HCI
SM
GATT
GAP
APP
ATT

## Slide 25: ATT – Client / Server Architecture
L2CAP
Servers have data, which are exposed using attributes
Clients want to use this data
The Client / Server role of a device is independent of the GAP central / peripheral role or the link layer master / slave role
It is possible for a device to act as both a client and server simultaneously, though the attributes on one device are independent of the attributes on the other device
Server
Client
ATT Requests or Commands
ATT Responses
Attribute
Attribute
Attribute
…
SM
GATT
ATT

## Slide 26: Generic Attribute Profile (GATT)
Designed for use by
  Application
  Profile
to enable an attribute client to communicate with attribute server
GATT defines:
  Procedures for using the attribute protocol:
    Discover attributes
    Read attributes
    Write attributes
    Obtain indications of these attributes
  The grouping and relationship of characteristics within a service or profile
  Procedures for configuring the broadcast of attributes
P
L2CAP
PHY
P
P
P
...
LL
HCI
SM
GATT
GAP
APP
ATT

## Slide 27: Profiles and Services
Heart Rate Profile
A Profile defines and describes the use of Services necessary to implement a given Application
Bluetooth SIG adopted examples:
  Heart Rate Profile
    Heart Rate Service (HRS)
    Device Information Service (DIS)
  Proximity Profile
    Link Loss Service
    Immediate Alert Service
  Find Me Profile
    Immidiate Alert Service
Profile
Service
Characteristic
Properties
Value
Descriptor
Characteristic
Properties
Value
Descriptor
...
HRS
Measurement
Notify
98
User. Disc.
GATT = Generic Attribute Profile
DIS
System ID
Read Only
XX ... XX
User. Disc.
Notes: Bluetooth low energy is designed for data sharing. To ensure interoperability, Bluetooth SIG has developed a set of application specific profiles. A Profile defines and describes the use of Services necessary to implement a given Application. One example is the Heart Rate Profile, developed and adopted by Bluetooth SIG and its members. This means that a Bluetooth Smart Ready device, such as a smartphone, can work with Bluetooth Smart heart rate sensors from different vendors. As the illustration shows, a profile is composed of one or more services with associated characteristics. For a heart rate sensor the profile would consist of a Heart Rate Service with measurement as the associated characteristic. In the example, the measurement shows a heart rate of 98. In addition, the heart rate profile also includes the Device Information Service which provides information about the device, for example System ID. Note that both of these adopted services includes several other mandatory characteristics even though they are not shown in the example. There are two different types of profiles, the profiles adopted by Bluetooth SIG and proprietary profiles. Bluetooth SIG has adopted profiles such as Proximity and Find Me. The Proximity profile has services as Link Loss and Immediate alert. As you can see, several profiles may implement the same type of services, in this example the Immediate Alert Service is used by both the Proximity and Find Me Profiles. Proprietary profiles are user specific profiles such as the TI SensorTag services which we will see later.

## Slide 28: GATT – Client / Server Architecture
GATT specifies the structure in which profile data is exchanged
Same client server architecture as Attribute Protocol, except that data is encapsulated in “Services” and data is exposed in “Characteristic”
Server
Client
Requests or Commands
Responses
Service
Characteristic
Characteristic
…
Service
Characteristic
Characteristic
…
ATT
SM
GAP
GATT

## Slide 29: GATT – Client
When two BLE devices are in the connected state, the GATT client device can perform several different sub-procedures to communicate with the GATT server device:
  Discover Characteristic by UUID: search the GATT server for all attributes with type that matches the specified UUID
  Read Characteristic Value: read the value of the characteristic at the specified handle
  Write Characteristic Value: write a new value to the characteristic at the specified handle
A GATT server device, when configured to do so, can send out messages to the GATT client device without being prompted:
  Notification: The value a characteristic is sent from the server to the client without receiving a read request, and does not need to be acknowledged
  Indication: The value a characteristic is sent from the server to the client without receiving a read request, but must be acknowledged before any further data can be sent
ATT
SM
GAP
GATT

## Slide 30: Generic Access Profile (GAP)
Defines generic procedures for connection-related services:
  Device Discovery
  Link Establishment
  Link Management
  Link Termination
  Initiation of security features
Many GAP functions correspond directly to the functions of the Link Layer in the controller
P
L2CAP
PHY
P
P
P
...
LL
HCI
SM
GATT
GAP
APP
ATT

## Slide 31: GAP - Roles
A Bluetooth low energy device can operate in four profile roles:
  Broadcaster
    An advertiser that is non-connectable
    Example: Temperature Sensor
  Observer
    Scans for advertisements, but cannot initiate connections
    Example: Temperature Display
  Peripheral
    An advertiser that is connectable
    Operates as a slave in a connection
    Example: Watch
  Central
    Scans for advertisements and initiates connections
    Operates as a master in connections.
    Example: Smart Phone
P
P
P
PHY
GAP
Notes: A Bluetooth low enrgy device can operate in four profile roles.
A Broadcaster is an advertiser that is non-connectable, for example a Temperature Sensor that transmits current temperature
An Observer scans for advertisements, but cannot initiate connections. This could be a Temperature display that receives temperature data and presents it on a screen.
A Peripheral device is an advertiser that is connectable and can operate as a slave in a single link layer connection This could for example be a watch or a heart rate sensor.
A central device scans for advertisements and initiates connections. It operates as a master in a single or multiple link layer connections. A good example is a Smart Phone or a PC.
Note that a Bluetooth low energy can operate in multiple roles at the same time: Supported ones are
Peripheral + Broadcaster
Peripheral + Observer
Central + Broadcaster
These device roles also explain how the Bluetooth low energy ecosystem is built up and how it is set up to interact with other devices.

## Slide 32: GAP – Multiple Roles
The BLE specification multiple-role configurations:
  Peripheral and Broadcaster
    device operates as a slave in a single link layer connection
    send out non-connectable advertisements
  Peripheral and Observer:
    device operates as a slave in a single link layer connection
    Scan for advertisements without initiating a connection
  Central and Broadcaster:
    Device scans for advertisements and initiates connections as a master
    Broadcast non-connectable advertisements
P
P
P
PHY
GAP

## Slide 33: Bluetooth Low Energy Ecosystem Overview

## Slide 34: BLE Interoperability
Our device/BLE stack has been tested with many other devices from different vendors
Minor differences in BLE features across vendors
iOS
  Apple guidelines
    30ms by default – not configurable in app
  Send connection parameter update
  Private resolvable address
Android
  New BLE feature release
  Android 5.0 supports Central/Peripheral
Debug using sniffer captures
Notes: TI provides a selection of powerful tools as part of the Bluetooth low energy software offering. BTool provides complete control of a connected network processor via a graphical user interface. It allows a developer to test every aspect of the Bluetooth low energy stack, including pass-key security, advertisement data, device whitelist, service discovery and more. The BLE Device Monitor is a windows application that displays all services and characteristics on any connected Bluetooth low energy device. It can also be used to read and write to the exposed characteristics. The TI SmartRF Protocol Packet Sniffer is a powerful development assistant which displays the Bluetooth low energy packets as they are sent over the air. This live view and the generated logs can be used for effective debugging during evaluation and development. The SmartRF Flash Programmer is a tool that can be used to program the flash memory of TI’s Bluetooth low energy devices and read out and change the IEEE [I Triple E] address of the device.

## Slide 35: Backup

## Slide 36: Bluetooth low energy Solutions
Bluetooth low energy SDK
Fully Featured BT4.0 LE Stack
BT 4.0 Qualified
Broadest range of certified profiles
Unique Features
  Over-the-air-download
  High throughput
miniBLEBroadcaster
Standalone Solution for CC2543
Size optimized BLE Broadcaster
Hardware
Software
 | CC2540 | CC2541 | CC2543
Max Output Power | +4dBm | 0 dBm | +5 dBm
TX current (0 dBm) | 26 mA | 18.2 mA | 26 mA
Flash | 128/256kB | 128/256kB | 32kB
Ram | 8kB | 8kB | 1kB
Sleep Timer | Crystal or RC | Crystal or RC | RC
Dual Boot | YES | YES | NO
Size | 40 pin 6x6 QFN | 40 pin 6x6 QFN | 32 pin 5x5 QFN
Key Benefits | Full BLE stack USB | Full BLE stack I2C | Broadcast Only Low Cost

## Slide 37: Bluetooth low energy Kits
CC2540DK-MINI
CC2541DK-MINI
The easiest
way of evaluating
Bluetooth low
energy
CC2543 Broadcaster / Beacon
Reference Design
Prototype Board
BLE broadcast Software
Low power, low cost
CC2541DK-SENSOR
Targeting Smart Phone App developers.
Provides sensor data
from 6 sensors
CC2541DK-RC
Operates as a multiple HID mouse, keyboard and RC
BLE Lighting
Reference Design
Prototype Board
iOS App
Development Kits on eStore.ti.com
Kits Available on Request
CC2540DK
CC2541EMK
Advanced development platform
BLE RC Voice
Reference Design
Prototype Board
Notes: Our various development kits target different applications and development approaches. The mini development-kits are two of our most widely used kits. The kits include a combined debugger and programmer, a USB dongle for profile debugging and packet sniffing, and a Keyfob with either a CC2540 or 41. The Keyfob is powered by a coin cell battery and has LEDs, buttons, a buzzer and an accelerometer. The USB-dongle can be used together with our powerful PC application, BTool. This kit is the typical beginners kit and comes with a great out of box experience and is an easy way to get started with Bluetooth low energy. The _more_ extensive CC2540 Development Kit targets more advanced developers. The development kit includes two CC2540 evaluation modules and two evaluation boards with sockets for the modules. With this kit you have the possibility to access more peripherals such as LCD, Joystick and serial interfaces. All pins on the chip are accessible on the evaluation board, making it suitable for more in depth testing and development. The kit is also suitable for RF measurements. The CC2541 Evaluation Module Kit, EMK, is an add-on to the development kit containing two CC2541 evaluation modules for use with the evaluation boards in the development kit. The SensorTag kit is a CC2541 solution with six different sensors which can be individually controlled by a Bluetooth Smart Ready phone or any other Bluetooth Smart ready device. The kit targets app developers who want an easy and fun entry into Bluetooth low energy application development. It’s also the perfect kit to evaluate adding mobile connectivity to your product. The Advanced Remote Control kit is a Bluetooth low energy remote control which implements the Bluetooth SIG adopted Human Interface Device profile, enabling seamless connection with Smart Ready devices supporting this profile, such as Windows 8 computers with Bluetooth 4 hardware. The remote uses inertial motion sensors for mouse control and has an IR LED and consumer control keys like play/pause as well as a numeric keypad. The entire application runs on the CC2541 system on chip.

## Slide 38: Additional Reference Features CC2640
TI Confidential - NDA Restrictions
Reference Designs
Software Features
Remote Control
PDM, NFC,
Voice, Motion,
Wireless Charging
HID Keyboard
Full BT4.1 support
IP over BLE
6LowPAN
Multiple Dev. Environments:
IAR, CCS, GCC
Master/Slave - Mesh
Flexible OTA Firmware Update (OAD)
Apple iBeacon
Apple HomeKit
Range Extender
BLE + CC2592
Up to +10dBm
Medical Designs
Heart Rate Dev. Pack for Sensor Tag
PulseOx Sensor
Wireless ECG
WiFi + BLE Gateway

## Slide 39: Bluetooth low energy Free Tools
BTool
Run and test all possible Bluetooth low energy functionality controlled from the PC tool.
BLE Device Monitor
Provides an intuitive and graphical way to explore Bluetooth low energy Services and Characteristics.
SmartRF™ Protocol Packet Sniffer
Capture Bluetooth low energy communication live with full overview.
SmartRF™ Flash Programmer
Program devices and Read/write IEEE addresses
Notes: TI provides a selection of powerful tools as part of the Bluetooth low energy software offering. BTool provides complete control of a connected network processor via a graphical user interface. It allows a developer to test every aspect of the Bluetooth low energy stack, including pass-key security, advertisement data, device whitelist, service discovery and more. The BLE Device Monitor is a windows application that displays all services and characteristics on any connected Bluetooth low energy device. It can also be used to read and write to the exposed characteristics. The TI SmartRF Protocol Packet Sniffer is a powerful development assistant which displays the Bluetooth low energy packets as they are sent over the air. This live view and the generated logs can be used for effective debugging during evaluation and development. The SmartRF Flash Programmer is a tool that can be used to program the flash memory of TI’s Bluetooth low energy devices and read out and change the IEEE [I Triple E] address of the device.

## Slide 40: More Cool Tools
Sensor Tag App
  GUI for connecting to and controlling the Sensor Tag and viewing graphs for different sensors.
MultiTool
  Allows connection to other devices besides Sensor Tags.
Notes: TI provides a selection of powerful tools as part of the Bluetooth low energy software offering. BTool provides complete control of a connected network processor via a graphical user interface. It allows a developer to test every aspect of the Bluetooth low energy stack, including pass-key security, advertisement data, device whitelist, service discovery and more. The BLE Device Monitor is a windows application that displays all services and characteristics on any connected Bluetooth low energy device. It can also be used to read and write to the exposed characteristics. The TI SmartRF Protocol Packet Sniffer is a powerful development assistant which displays the Bluetooth low energy packets as they are sent over the air. This live view and the generated logs can be used for effective debugging during evaluation and development. The SmartRF Flash Programmer is a tool that can be used to program the flash memory of TI’s Bluetooth low energy devices and read out and change the IEEE [I Triple E] address of the device.

## Slide 41: Bluetooth 4.2 – What is it?
BT 4.2 is the latest version of the Bluetooth Core Specification. It was officially adopted by the BT SIG on December 3, 2014.
Main new features being added in BT 4.2:
  LE Secure Connections
    Based on Diffie-Helman Key Exchange, similar to the Secure Simple Pairing feature in classic Bluetooth
    Closes the well-known security holes in BLE that exist in the BT 4.0/4.1 specs
  LE Privacy 1.2
    Keeps BLE devices from being tracked
    Significant improvement over the confusing and little-used privacy features in BT 4.0/4.1 (which are being deprecated)
  LE Data Length Extension
    Increases data throughput by up to 2.5x by increasing the packet capacity by 10x
IPv6-over-BLE is not an actual feature of BT 4.2; however two BLE profiles (which will be based on BT 4.2 features), targeted for adoption in late 2014 or early 2015, will enable this.
BT 4.2 does not include any mesh support; for now any BLE mesh systems that are being used are not based on any Bluetooth standard.
It will probably take a while for phones and other Bluetooth Smart Ready devices to add support for BT 4.2 (most don’t even support BT 4.1 yet), so the features of BT 4.2 would not really be useful right now unless you are working in a closed system with only BT 4.2 enabled devices.
TI Confidential – NDA Restrictions

## Slide 42: Bluetooth 4.2 – TI Status
CC2540 / CC2541
  Currently only supports BT 4.0
  Possibility to add some (but not all) BT 4.1 features to CC254x in 2015
  No BT 4.2 support is planned for CC254x. This is mainly due to the limited processing capabilities and RAM on the CC254x. In addition, the CC254x radio core does not support the PHY requirements for the higher data rates in BT 4.2
CC2640 / CC2650
  Will have full support for BT 4.1 at RTM in February
  Hardware is fully capable of supporting all BT 4.2 features. We will be working on BT 4.2 software in 2015 (schedule TBD)
TI Confidential – NDA Restrictions